COMPONENT CHANGE APPLICATION

| Customer | STURM! | Customer model | RH2592P |
| --- | --- | --- | --- |
| Factory | BORUI | Factory model | Z1A2-26SRE |
| The first changed component order number | STURM ! RU120209CC-H |
| Change purpose | In order to reduce shake of drill bit, reduce the clearance between drill bit cover (10) and connect pipe (34), and rotary sleeve assembly is integrative. |
| Change detail | Please refer to below details. |
| Dis-interchange components | Drill bit cover(10 in exploded view), O- ring (11 in exploded view), Position pin(33 in exploded view), connect pipe(34 in exploded view), But Rotary sleeve assembly is same, can interchange. |

Change pictures:

| Old: drill bit cover(10 in exploded view), O- ring (11 in exploded view), Position pin(33 in exploded view), connect pipe(34 in exploded view) | New: drill bit cover(10N in exploded view), snap ring (11N in exploded view), connect pipe(34N in exploded view) Rotary sleeve assembly (101N in new exploded view) |
| --- | --- |
| The left is new drill bit cover(10N) and snap ring(11N); The right is old drill bit cover(10), snap ring(11) and position pin(33). | The left is new rotary sleeve assembly(101N), The right is old rotary sleeve assembly, They can interchange. |
| Old drill bit cover(10 in exploded view), outer diameter is 25.1mm. | new drill bit cover(10N in exploded view), outer diameter is 25.2mm. |