COMPONENT CHANGE APPLICATION

| Customer | STURM! | Customer model | AG95151P, USM-95151P |
| --- | --- | --- | --- |
| Factory | Huali | Application date | Nov.01,2016 |
| The first changed component order number | UK160906. |
| Change purpose | To improve motor quality, increase the service life. |
| Change detail | Change the commutator diameter to 28.5mm; Change the length of brush holder from 32.2mm to 31.5mm; The motor fan insert a bush; Change the hole of middle cover diameter from 22 to 24mm. |
| Dis-interchange components | All modified parts can be used to repair the original machines. We revised the exploded view and parts list.(the parts no. are added “N”.) |

Change pictures:

| Original | Modified |
| --- | --- |
| Commutator diameter :27mm | Commutator diameter :28.5mm |
| Motor fan without bush insert | Motor fan with bush insert |
| the length of brush holder:32.2mm | the length of brush holder:31.5mm |
| middle cover diameter:22mm | middle cover diameter:24mm |